ESTIMATION OF LAND SURFACE TEMPERATURE USING LANDSAT TM  THERMAL INFRARED IN SELANGOR-NEGERI SEMBILAN

Asmala Ahmad1, Noorazuan Md Hashim2 & Zolkepli Buang3

1Jabatan Sains & Matematik

Pusat Perkhidmatan Akademik

Kolej Universiti Teknikal Kebangsaan Malaysia (KUTKM)

2Pusat Pengajian Sosial, Pembangunan & Persekitaran

Universiti Kebangsaan Malaysia (UKM), Bangi

3Pusat Kecemerlangan Pengajaran dan Pembelajaran

Kolej Universiti Teknikal Kebangsaan Malaysia (KUTKM)

Abstract

A full-scene of Landsat TM acquired on April 17, 1988 (path 127/row58) was used in this study. This scene covers the areas of Selangor and north part of Negeri Sembilan in Peninsular Malaysia. The main objective of this study is to evaluate the use of remote sensed information, especially thermal band 6 to gain land surface temperature (LST) using thermal band of Landsat images. The result will be compared with urban and non-urban surfaces by using normalised difference vegetation index (NDVI) and compare relationships between them.  The initial result showed that the correlation between the LST and the NDVI over ten locations in the study area is quite significant. The derivation of LST map using remote sensing technique in this study is useful in providing information for analysing geophysical parameters over Selangor-Negeri Sembilan area, especially dealing with the urban heat island phenomenon.

# Key Words

Landsat, Thermal band, LST, Emmisivity, NDVI

# 1	Introduction

Land-surface temperature (LST) can be defined as the thermal emission from the landscape "surface", including the top of the canopy for vegetated surfaces as well as other surfaces (such as bare soils). LST is an important parameter in the field of atmospheric sciences as it combines the result of all surface-atmosphere interaction and energy fluxes between the ground and the atmosphere and is, therefore, a good indicator of the energy balance at the Earth’s surface (Wan and Snyder, 1996).

LST controls the surface heat and water exchange with atmosphere. Estimation of LST from satellites infrared radiometers has been proven useful. Most studies have focused on the use of polar orbiting satellite systems because of their high spatial resolution (Sun et al., 2004).

One of the well known remote sensing satellite for natural resources and environmental applications is Landsat satellite series. Currently there are Landsat 5 TM which are operating  for this puposes. In this study Landsat 5 TM was used in order to estimate LST over Selangor – Negeri Sembilan area (Figure 1).

Figure 1. Area under study (shaded)

2	Data

This study used data recorded from a remote sensing satellite that was developed by NASA of USA - Landsat 5. Landsat 5 platform carries along the so called TM sensor, which is an advanced, multispectral scanning, Earth resources instrument designed to achieve higher image resolution, sharper spectral separation, improved geometric fidelity, and greater radiometric accuracy and resolution. The TM data are scanned simultaneously in seven spectral bands. Band 6 scans thermal (heat) infrared radiation. For this study, the data was recorded on April 17, 1988 for path 127/row58 (Figure 1). Spectral range of the all seven bands is shown in Table 1.

Table 1. Spectral range of bands and spatial resolution for the Landsat 5 TM sensor

| Band | Spectral Range | Spatial Resolution |
| --- | --- | --- |
|  | (Micrometer) | (Meters) |
| Band 1 | 0.45 - 0.52 | 30 |
| Band 2 | 0.52 - 0.60 | 30 |
| Band 3 | 0.63 - 0.69 | 30 |
| Band 4 | 0.76 - 0.90 | 30 |
| Band 5 | 1.55 - 1.75 | 30 |
| Band 6 | 10.40 - 12.50 | 120 |
| Band 7 | 2.08 - 2.35 | 30 |

# 2	Methodology

In order to estimate LST from Landsat data, the methodology in this study will be divided into four phase: (1) Data Calibration, (2) Conversion from Radiance to Brightness Temperature, (3) LST retrieval and NDVI retrieval.

### 2.1 Conversion from Digital Number to Radiance

All TM bands are quantized as 8 bit data thus, all information is stored in digital number (DN) with range between  0 to 255. The data was converted to radiance using a linear equation as shown below:

(1)

Where:

CVR is the cell value as radiance

CVDN is the cell value digital number

G is the gain (0.005632156 for TM6 and 0.003705882 for ETM+6)

B is the offset (0.1238 for TM6 and 0.3200 for ETM 6)

### 2.2 Conversion from Radiance to Brightness Temperature

By applying the inverse of the Planck function, thermal bands radiance values was converted to brightness temperature value.

(2)

Where:

T is degrees Kelvin

CVR is the cell value as radiance

K1 is calibration constant 1 (607.76 for TM) and (666.09 for ETM+)

K2 is calibration constant  2 (1260.56 for TM) and (1282.71 for ETM+)

# 2.3 LST Retrieval

LST was derived from TM6 using model developed by Qin et al. (2001) which uses the atmospheric water vapor and the near-surface air temperature on the mono-window algorithm for retrieving the LST. The surface emmissivity was fixed at 0.98 (Hadi et al., 1997). The atmospheric transmissivity was calculated using LOWTRAN 7 developed by Kneizys et al. (1989).

(3)

Where

C = es, where e is the land surface emissivity (e = 0.98 for Malaysia),

s = the total atmospheric transmissivity (s = 0.021 from LOWTRAN 7)

D=(1 _s)[1+(1 _e)s],

a = -67.355351,

b = 0.458606, and

Tsensor =  the sensor brightness temperature,

Ta represents the mean atmospheric temperature for Tropical Climate given by

Ta=17.9769+0.91715•T0 									(4)

T0 is near surface air temperature (300.45 K for Malaysia)

# 2.4 NDVI Retrieval

A vegetative index is a value that is derived from sets of remotely-sensed data that is used to quantify the vegetative cover on the Earth's surface. The NDVI is calculated as a ratio between measured reflectivity in the red and near infrared portions of the electromagnetic spectrum. These two spectral bands are chosen because they are most affected by the absorption of chlorophyll in leafy green vegetation and by the density of green vegetation on the surface. Also, in red and near-infrared bands, the contrast between vegetation and soil is at a maximum.

The Thematic Mapper bands 3  and 4 provide red and near-infrared measurements respectively and therefore can be used to generate NDVI data sets with the following formula:

(4)

- Result

Combination of band 3, 2 and 1 in red, green and blue channel was used to show the area in its natural colour (Figure 2). Masking of clouds and water bodies into black colour were carried out prior to any other processes. Original band used in deriving LST consist of pixels in digital number (Figure 3). The result of applying equation 1 which converts the digital number to radiance is shown in Figure 4.  By applying equation 2 the radiance image was converted to brightness temperature image as in Figure 5. Finally the LST image in Kelvin was obtained by applying equation 3. NDVI image was derived using equation 4. The pixels on both the LST and the NDVI image was density sliced in order to produce colour maps based on the different ranges of the pixels value. The NDVI image will be used later in determining relationship between LST and NDVI image.

Figure 2. Combination of TM band 3,2,1 in red, green, and blue channel

Figure 3. TM band 6 in DN

Figure 4. TM band 6 in radiance

Figure 4. TM band 6 in brightness temperature

|  | LST (Kelvin) |
| --- | --- |
|  |  | 40-50 |
|  |  | 51-10 |
|  |  | 101-200 |
|  |  | 201-300 |
|  |  | 301-400 |
|  |  | 401-500 |
|  |  | Clouds, water |
| Figure 5. Map of LST |  |

|  | NDVI |
| --- | --- |
|  |  | < 0.2 |
|  |  | 0.2 – 0.4 |
|  |  | 0.4 - 0.5 |
|  |  | > 0.5 |
|  | NDVI < 0.2 0.2<NDVI<0.5 NDVI > 0.5 | Bare soil Mixture bare soil&vegetation Fully vegetated |
| Figure 6. Map of NDVI |  |  |

# 4	Relationship Between LST and NDVI

In order to find the relation ship between LST and NDVI, 10 locations in the in the study area were determined (Table 2). A graph of LST vs. NDVI was plotted as shown in Figure 7.

##### Table 2. LST and NDVI measurement at several locations

| Location (Universal Traverse Mercator Projection) | LST (K) | NDVI |
| --- | --- | --- |
| Eastern | Northen |  |  |
| 335483.776 | 411518.787 | 182.21 | 0.4728 |
| 372626.633 | 401335.662 | 378.83 | 0.3282 |
| 375891.939 | 370378.963 | 314.01 | 0.5804 |
| 418749.082 | 391559.862 | 248.48 | 0.5238 |
| 456300.102 | 387079.28 | 335.70 | 0.5121 |
| 394259.286 | 347161.438 | 506.44 | 0.4803 |
| 411810.306 | 350012.713 | 631.46 | 0.0270 |
| 390585.81 | 298689.763 | 159.95 | 0.6000 |
| 451810.306 | 336570.987 | 292.25 | 0.5726 |
| 437932.755 | 298282.438 | 485.36 | 0.2222 |

Figure 7. Relationship between LST and NDVI

# 5	Conclusion

The result shows that estimation of land surface temperature using thermal band 6 of Landsat 5 satellite gives a promising result. Relationship between LST and NDVI based on 10 locations can be shown as linear model y = -651.75x + 634.98 with R2 = 0.6465.  Future study will include comparison between satellite measurement and  insitu readings using conventional instruments.

References

- Hadi Batatia and Nabil Bessaih (1997). Satellite Land Surface Temperature for Sarawak Area. Proceedings of the 1997 Asian Conference on Remote sensing. Global Environment Session.

- Kneizys, F.X., Shettle, E.P., Gallery, W.O., Chetwynd, J.H., Abren, L.W., Selby, J.E.A., Clough, S.A. and Fern, R.M. (1989). Atmospheric Transmittance/Radiance: Computer Code LOWTRAN 7. Hanscom Air Base, Massachusetts : U.S. Air Force Geophysical Laboratory.

- Qin, Z., Karnieli, A., & Berliner, P. (2001). A mono-window algorithm for retrieving land surface temperature from Landsat TM data and its application to the Israel–Egypt border region. International Journal of Remote Sensing. 22(18), 3719–3746.

- Sun, D. and Pinker, T. (2004). Case study of Soil Moisture effect on Land Surface Temperature Retrieval. IEEE Geoscience And Remote Sensing Letters. Vol. 1. No. 2 : 127 – 130.

- Wan, Z and Snyder, W. (1996). MODIS Land-surface Temperature Algorithm Theoretical Basis Document (LST ATBD): version 3.2.